New generation of TWIN H.D.  PVR BOX

English (export) version

INDEX

1

INDEX	3

Precautions	5

1.Important Safety Instructions	5

2.Notice	5

3.Copyright
	6

4.Disclaimer	6

5.Trademarks	6

7

Before You Begin	8

1.Main Features	8

1.Accessories	9

Hardware Description	10

1.Front Panel Configuration	10

1.VFD(Vacuum Fluorescent Display)	11

2.Rear Panel Configuration	12

3.Remote Control Unit	14

4.Multi-Brand IR Remote Controller Setting	18

Connections Diagram	19

1.Receiver to TV with Digital A/V Output	19

1.Receiver to TV With Analog A/V Output	20

2.Receiver to TV and VCR	21

3.Connecting to Dish	21

4.1Connecting by Loop through
	21

4.2Connecting each Dish to each Tuner
	22

4.3Connecting Antenna cable to each Tuner using DiSEqC SW (Recommend)
	22

Guide of Functions	23

1.Selecting a Service	23

1.1Using CH UP/DOWN buttons	23

1.2Using Service List	23

1.3Using Instant Service List	23

1.4Using Recent Service List	24

2.Information Window	24

3.Multi-Picture Display. (*)	24

4.Electronic Program Guide (EPG)	24

5.Favorite Group	26

6.Volume Control	26

7.Pause	26

8.Subtitle	26

9.Audio Track	28

10.Teletext	28

11.PIP (Picture in Picture)	28

PVR (Personal Video Recorder) Function	33

1.Recording	33

1.1Recording methods  	33

1.2Recording Edit 	35

1.3Long Time recording 	35

1.4Pause during recording 	35

2.Time Shifting	37

3.Playback (Play List)	39

3.1Play List	39

3.2MP3 Player	39

3.3Image Viewer	40

4.Bookmark	40

5.Trick mode	42

Guide of Main Menu	43

1.System Tools
	43

1.1Storage Manager	43

1.2Timer Manager	43

1.3Service List manager	45

1.4Data Transfer	46

2.Configuration	47

2.1Recording Option	47

2.2Parental Control	47

2.3UI (User Interface) Setting	49

2.4Time Setting	49

2.5Language Setting	50

2.6A/V Output Setting	51

3.Installation	53

3.1Dish Setting	53

3.2Positioner Setting	55

3.3Service Search	55

3.4Network Setting 	58

3.5System Recovery	58

3.6System Information	59

4.Utilities	60

4.1Calculator	60

4.2Calendar	60

4.3CAS (Conditional Access System)	60

Troubleshooting	62

Specifications	63

Code Table for Universal Remote Control Unit
	65

1.Key Table	65

2.TV Brands	67

3.VCR Brands	74

4.DVD Brands	79

Menu Map	83

Precautions

  - Important Safety Instructions

- Read these instructions.

- Keep these instructions.

- Heed all warnings.

- Follow all instructions.

- Do not use this apparatus near water.

- Clean only with dry cloth.

- Do not block any ventilation openings. Install in accordance with the manufacturer’s instructions.

- Do not install near any heat sources such as radiators, heat registers, stoves, or other apparatus (including amplifiers) that produce heat.

- Do not reverse the safety purpose of the polarized or grounding-type plug. A polarized plug has two blades with one wider than the other. A grounding type plug has two blades and a third grounding prong. The wide blade or third prong is provided for your safety. If the provided plug does not fit into your outlet, consult an electrician for replacement of the obsolete outlet.

- Protect the power cord from being walked on or pinched particularly at plugs, convenience receptacles, and the point where they exit from the apparatus.

- Only use attachments/accessories specified by the manufacturer.

- Use only with the cart, stand, tripod, bracket, or table specified by the manufacturer, or sold with the apparatus. When a cart is used, use caution when moving the cart/apparatus combination to avoid injury from tip-over.

- Unplug this apparatus during lightning storms or when unused for long periods of time.

- Refer all servicing to qualified service personnel. Servicing is required when the apparatus has been damaged in any way, such as power-supply cord or plug is damaged, liquid has been spilled or objects have fallen into the apparatus, the apparatus has been exposed to rain or moisture, does not operate normally, or has been dropped.

WARNING : To Prevent fire or shock hazard do not expose the set to rain or moisture.

  - Notice

- These servicing instructions are for use by qualified service personnel only. To reduce the risk of electric shock, do not perform any servicing other than that contained in the operating instructions unless you are qualified to do so.

- The apparatus shall not be exposed to dripping or splashing and that no objects filled with liquids, such as vases, shall be placed on the apparatus.

- The mains plug is used as the disconnect device. The disconnect device shall remain readily operable.

|  | To reduce the risk of electric shock, do not remove the cover (or back). No user serviceable parts are inside. Refer servicing to qualified service personnel. |
| --- | --- |
|  | The Lightning Flash with arrowhead symbol within an equilateral triangle, is intended to alert the user to the presence of un-insulated "dangerous voltage" within the product enclosure that may be of sufficient magnitude to constitute a risk of shock to persons |  | The exclamation point within an equilateral triangle is intended to alert the user to the presence of important operating and maintenance (servicing) instructions in the literature accompanying the product |

  - Copyright

This manual is protected by copyright laws.

Copy, use and reproduction of this manual in part or whole without FORTIS's prior written approval are prohibited.

  - Disclaimer

The manufacturers, distributors and agents are not liable to any kind of damage caused by the use of the information contained in this manual.

The instruction and descriptions which this manual contains are based on the time of this manual's production.

The manufacturer constantly updates it with new functions and technology.

All the specifications are subject to change without prior notice.

  - Trademarks

HDMI, the HDMI logo and High-Definition Multimedia Interface are trademarks or registered trademarks of HDMI Licensing LLC

Dolby is a trademark of Dolby Laboratories

Dolby and the ‘double-D’ symbol are trademarks of Dolby Laboratories

Before You Begin

- Main Features

- Twin Tuner HDTV PVR Receiver ( H.264/ MPEG4 HD )

- Supports MPEG4 /MPEG2 - HD/SD, DVB-S2 /DVB-S

- Powerful compatibility through Embedded Linux OS

- Time Shifting, Recording & Playback with External HDD (SATA) / External HDD (USB 2.0)

- Simultaneously Records 2 Services and allows Watching 2 others (PIP)

- Powerful Extended EPG supports and Event Recording

- Two USB 2.0 Host ports (MP3 Player & JPEG Viewer)

- Xvid file play back supported

- Ethernet port Supported

- Intelligent Blind Scan for both SD and HD TV & Multi-Satellite Search

- Premium Grade White VFD Display (12 Digit Alphanumeric)

- Premium Grade Universal remote control unit

- Multi-LNB Controlled by DiSEqC Control Version 1.0, 1.1, 1.2 and USALS

- On-Screen Display with Full Color & Resolution

- Favorite Service Groups

- Powerful Service Control by Favorites, Lock, Skip, Move and Delete

- Service Sorting by Alphabet, Transponder and CAS

- User Friendly & Multi-language Supported (OSD & Menu)

- Teletext / Subtitle Supported

- Maximum 10,000 Services Programmable

- PIP & Multi-picture Display(*)

- Parental Lock / System Lock / Installation Lock

- HDMI Video & Audio Output (576i, 576p, 720p, 1080i)

- Supports Y/Pb/Pr(component) Output in HD

- CVBS(composite) Video & Audio Output via RCA

- CVBS, RGB, Y/C Video & Audio Output via TV SCRAT

- Optical Output for Digital Audio(SPDIF)

- MPEG-II Digital & Fully DVB Compliant

- Software & Service channel Database upgrade via USB & RS-232C port

- 1 Smart card reader and 2 Common Interface Slots

- 1W Stand-by Power Consumption

NOTE : (*) This feature(Multi-picture Display) will be supported later, by new s/w version by upgrading.  Please refer to your local dealer / distributor.

  - Accessories

NOTE : If any accessories listed above are missing, contact the sales representative where you purchased this unit.

Hardware Description

- Front Panel Configuration

- POWER BUTTON : Press to switch between STANDBY and POWER ON modes.

- Vol Up/Down button: Press to change audio volume in normal mode or to navigate menu in menu mode.

- CH Up/Down button : Press to change services in normal mode, or to move highlighted-bar in menu mode.

- Remote Sensor : Receives signal from remote controller.

- VFD Display : The VFD consist of 12-digit letter and various icons. These letters and icon display the current status of receiver such as service name, service information and so on.

- USB(Front) : Use it when connecting to external USB storage device.

- SMART CARD READER : Insert smart card for encrypted service access.

- PCMCIA : To receive pay-tv service you need a CA-Module and a smart card from the service provider.

  - VFD(Vacuum Fluorescent Display)

- Remote Indication LED : The LED lights on when a key on the Remote Controller is pressed.

- Radio icon : The icon lights on when it is change the radio service.

- TV icon : The icon lights on when it is change the TV service.

- SAT : Satellite mode.

- TER(Option) : Terrestrial mode.

- FILE : Turn on when file list is displayed in the SATA HDD or USB Storage Device.

- REC : Turned on during recording.

- PLAY Mode : Turn on when you play the file on file list. (SATA HDD, USB Storage Device)

- TIME SHIFT : Turned on during Time-shift.

- Information : Display information including service name and other information.

- TIMER : Turned on during timer is set.

- HD : Turned on during HD service.

- USB : Turned on during USB device working.

- LOCK : Turned on during lock service.

- Dolby : Turned on during Dolby service.

- Tu1 : Turned on during used Tuner1

- Tu2 : Turned on during used Tuner2

- MP3 : Turned on during MP3 listen.

- Repetition(*) : Turned on during recording repeatedly.

- Resolution : Turned on during Resolution setting.

NOTE : (*) This icon(Repetition) will be supported later, by new s/w version by upgrading.  Please refer to your local dealer / distributor.

  - Rear Panel Configuration

- LNB IN_1 
Satellite broadcasting signal input socket for the first tuner. Connects a satellite antenna cable.

- LNB OUT_1  
Satellite broadcasting signal output socket through the first tuner. Connects a STB for loop-through.

- LNB IN_2 : 
Satellite broadcasting signal input socket for the second tuner. Connects a satellite antenna cable.

- LNB OUT_2 : 
Satellite broadcasting signal output socket through the second tuner. Connects a another STB for loop-through.

- SPDIF : Connects to the audio system using a S/PDIF cable. (digital audio)

- VIDEO : Connects to the TV or VCR using a RCA cable. (Composite video output / Yellow)

- AUDIO L/R : Connects to the TV or VCR using a RCA cable. (Stereo audio output / White, Red)

- Component : Connects to the TV or VCR using a component cable. ( YPbPr)

- VCR SCART : Connects to the VCR or DVD using a VCR SCART cable.

- TV SCART : Connects to the TV using a TV SCART cable.

- USB : Use it when connecting to external USB storage device.

- HDMI : Connects to the TV by using a HDMI cable for the best quality picture and audio.

- Ethernet : Local area network port.

- RS-232C : Serial port for firmware update and data transfer.

- e-SATA : Use it when connecting to external SATA HDD.

- A/C Switch : Power switch

  - Remote Control Unit

  - POWER : Turns the STB On/Off.

  - MUTE : Turns the sound On/Off.

  - Universal Buttons

    - Universal TV : Change the TV Remote Controller.

    - STB : Change the STB Remote Controller.

    - Universal DVD : Change the DVD Remote Controller.

  - MODE

    - V.Format : To select the TV types.(PAL/NTSC)

    - Sleep : To adjust sleep timer.

    - TV/RADIO : Switches between TV and Radio.

    - Resolution : To select the resolution format. Each time you press the Resolution button, the resolution changes in the following sequence: 576i > 576p > 720p > 1080i

  - Playback Control Buttons

    - Rewind : Rewinds at high speed. Each time you press this button the rewind speed is increased.

    - Fast Forward : Fasts forward at high speed. Each time you press this button the speed is increased.

    - Previous File : To play the previous MP3 file in MP3 play mode. This button is also used to jump back to beginning of recording during a playback.

    - Next File : To play the next file. This button is also used to jump to end of recording during a playback.

    - Play / Time shift : Display the progress bar of playback when no progress bar is displayed. Start playback with normal speed. Return to normal speed from trick mode..

    - Recording : To start Recording.

    - Repetition (*): This key is used to play back a recording repeatedly.

    - Pause : This key is used to pause the video. Press once more to resume the video.

    - STOP : To stop time shifting, play back or recording.

NOTE : (*) This button(Repetition) will be supported later, by new s/w version by upgrading.  Please refer to your local dealer / distributor.

  - Color Buttons

    - RED : Used for special function in menu. RED key is used to sort lists in service list or go to previous day search in EPG or make/delete the current position as a bookmark.

    - GREEN : Used for special function in menu. Green key is used to set favorites setting in service list or go to the next bookmark position.

    - YELLOW : Used for special function in menu. Yellow key is used to find service in service list or change the audio track.

    - BLUE : Used for special function in menu. Blue key is used to set service list option in service list or display Multi-Picture.(*)

  - Information : Shows the information of the current program. If you press one more, detail information box will be shown.

  - Recall : Moves to previous service.

  - ARROW Buttons

    - Up & Down Buttons : To change the value of a selected item with preprogrammed values in menu.

    - Left & Right Buttons : To move the cursor left and right in menu.

  - OK or Service List : Show the service list in non-menu mode and select an item or confirm in menu mode.

  - Menu : To enter the main menu or to move to the previous menu.

  - EXIT : Exit from the menu or pop-up window.

  - Page Up& Down : Move to the next or previous page if more than one page are available. This button also is change the location of sub picture in PIP.

  - Favorite : To display the satellite group and the favorite groups.

NOTE : (*) This Feature(Multi-Picture) will be supported later, by new s/w version by upgrading.  Please refer to your local dealer / distributor.

  - Volume Up & Down : To change the Volume.

  - Channel Up & Down: To change service channel.

  - EPG(Electronic Program Guide) : Show the TV/Radio program guide.

  - Play List : To show the file list in the SATA HDD or USB Storage Device.

  - PIP Buttons

    - PIP(Picture in Picture) : To set PIP window.

    - PIP Swap : Switching between main-picture and sub-picture

    - PIP(Picture in Picture) Service List : To shown the sub-picture service list.

  - Numeric : Controls the numerical operation and service numbers directly.

  - Subtitle : To show multilingual subtitle.

  - Teletext : To show the digital teletext.

  - Multi-Brand IR Remote Controller Setting

NOTE : When there is no input during about 10 seconds from set mode, set mode is canceled.

- Direct Code Entry

Step 1 : Turn on the DEVICE what you want to set up(TV / DVD / VCR)

Step 2 : Press DEVICE and OK button during about 2 seconds at the same time.

              - DEVICE LED will blink twice.

Step 3 : Input 3 digit code numbers. (Refer to ‘Code Table for Universal Remote Control Unit’)

              - DEVICE LED will blink twice and the DEVICE turns off.

              - If you enter wrong DEVICE code, DEVICE will blink once

Step 4 : If your DEVICE turns off, press OK button.

              - DEVICE LED will blink twice.

- Auto Code Search

Step 1 : Turn on the DEVICE what you want to set up(TV, DVD)

Step 2 : Press DEVICE and OK button during about 2 seconds at the same time.

              - DEVICE LED will blink twice.

Step 3 : Press UP or Down button within 10 seconds to enter the Search mode.

Step 4 : Press UP or Down button until DEVICE turns off, one and one.

Step 5 : If your DEVICE turns off, press OK button.

              - DEVICE LED will blink twice.

- Code No. Checking (Number Call)

Step 1 : Press DEVICE and OK button during about 2 seconds at the same time.

              - DEVICE LED will blink twice.

Step 2 : Press INFO button within 3 seconds.

              - LED will blink according to inputted mode number on the device.

( Case of digit '0', it blinks 10 times.)

Connections Diagram

- Receiver to TV with Digital A/V Output

- Connect the satellite antenna cable to LNB IN.

- Connect the HDMI Cable to HDMI Connector of TV.

- Connect SPDIF to Digital audio input of the equipment(Digital Audio)

NOTE : Depending on the A/V equipment you own, there are various ways you can connect the STB. To choose the best connection option, please refer to the manual of equipment you would like to connect to. To get High Definition playback of High Definition content, we recommend that you connect your high definition display with a HDMI cable. HDMI supports standard, enhanced or high-definition video and multichannel audio in a single cable.

  - Receiver to TV With Analog A/V Output

- Connect the satellite antenna cable to LNB IN.

- Connect the TV SCART to SCART of TV.

- Connect the VCR SCART to SCART of VCR.

- Connect the Component to Component of TV.

- Connect the RCA to RCA of TV.

NOTE : The component connection(YPbPr) is recommended for Digital TV.
The SCART cable connection is recommended for analogue TV or VCR
The composite connection(RCA cable) is recommended for analogue TV
You cannot view high definition video with the SCART and the composite video connector.

  - Receiver to TV and VCR

- Connect the satellite antenna cable to LNB IN.

- Connect the TV SCART to SCART of TV.

- Connect the VCR SCART to SCART of VCR.

  - Connecting to Dish

  - Connecting by Loop through

  - Connecting each Dish to each Tuner

  - Connecting Antenna cable to each Tuner using DiSEqC SW (Recommend)

Guide of Functions

- Selecting a Service

To select the desired service (channel), please refer to below instructions.

  - Using CH UP/DOWN buttons

You can navigate between services by pressing CH UP/DOWN buttons. Whenever you press the CH UP(DOWN) button, current service will be changed to next/previous service. Please press CH UP or CH DOWN button until you fine the service you want to watch.

  - Using Service List

To select the desired service in the service list, you should firstly display the service list pressing OK button.

Use ARROW buttons to select a desired service and press OK button. 
You can see that the service is changed in small screen on the top-right. 
To watch the service, press OK button once more.
To watch the previous service, press EXIT button.
In the Service List window, you can also use additional functions with COLOR buttons.
Press RED button, you can sort the services by Alphabet, Transponder(TP), Group, Tuner and CAS (Conditional Access System).
Press GREEN button, you can add the services to one of 10 favorite List.
Press YELLOW button, you can search & find the service with virtual keyboard.

Press BLUE button, you can adjust service list option.

NOTE : If you connect tuner with loop-through, you cannot use sort list option.

  - Using Instant Service List

- If you press NUMERIC buttons or UP/DOWN ARROW button, instant service list will be displayed.

- Select the desired service by using the ARROW button, and press OK button to watch.

- You can also enter the service number directly by using the NUMERIC button.

  - Using Recent Service List

- To return to the previous service that you were watching, press RECALL button for a short time.

- To display recent service list, press the RECALL button for a little bit longer time.

- To chose the service from the Recent Service List, use ARROW button to select, then press OK button.

- Press EXIT button to exit from the recent service list.

- Information Window

If you want to view the information of the current service that you are watching, press INFO button. Then the Information window will be displayed.
This Information window is automatically displayed when changing between the services.  This window contains much useful information such as service number, service name, scrambled types of service, teletext, subtitle, Audio indication for Dolby Digital, Time duration of service and so on.
By pressing INFO button once again, you can get more detailed information about the service.

- Multi-Picture Display. (*)

Press the BLUE button to display multiple pictures and use RED button to choosing the display options for 9 or 12 multiple pictures.

NOTE : (*) This feature will be supported later, by new s/w version by upgrading.  Please refer to your local dealer / distributor.

- Electronic Program Guide (EPG)

Electronic Program Guide (EPG) helps you to navigate through all the possible viewing options. And the EPG supplies additional information of channel service, such as program listings, start/end times and detailed information about the program listings for all available services.
The availability and size of information of these program details can be varied, depending on the particular broadcasters, individual services.

- Press EPG button, then the EPG menu will be displayed.

- Use the ARROW buttons to move to other services or to see previous/next guide.

- Press EPG button once to view full EPG with service list, and press it twice to view the additional EPG information of the channel service.  Keep pressing of EPG button will toggle between the full and detailed menus of EPG.

- Press GREEN button to view next day EPG and RED button to view EPG for previous day.

- Select the program by using the ARROW buttons then set the event timer by pressing OK.

- You can make a reservation for recording on EPG menu.

        - Press RECORD button to reserve the event. This reservation can be checked in the menu of Timer Manager, in the System tool menu.

        - To cancel the reservation for recording, press the OK button at the appointed event.

        - To edit the reservation for recording, press the RECORD button at the appointed event.

- Favorite Group

Select the FAV (Favorite) to view all favorite groups such as sports, movie, drama, satellite group and so on. Scroll through the various favorite group using the ARROW buttons, and select the desired favorite group by pressing OK.

- Volume Control

- To adjust the audio volume, press the VOL UP/ DOWN buttons.

- Audio volume control bar will be displayed in top of the screen and disappear after 4 seconds.

- When necessary, press MUTE button to turn on/off the audio sound.

NOTE : The mute function remains set while you change services.

- Pause

The PAUSE button is used to freeze the video. Press PAUSE button once more to resume the video.

- Subtitle

You can select the language for a Subtitle, if the program provides subtitle information.

- Press the SUBTITLE button on your remote control unit.

- Select the desired subtitle language then press OK button.

- The subtitle will be displayed in the selected language at the bottom of the screen.

- To turn OFF the subtitle from the screen, Select ‘Off’ from the subtitle language list.

NOTE : When program does not provide subtitle information, SUBTITLE button is not available.

- Audio Track

User can select the audio language list by pressing the AUDIO button.  Use the ARROW buttons to choose the preferred audio track from the list, then press OK to change.

- Teletext

When the TELETEXT icon on INFO Banner is appeared (Activated), Press the TELETEXT button to view the teletext information.

- PIP (Picture in Picture)

- When you press PIP button, sub picture screen will appear on the main screen view.
If you press PIP button one more time, primary picture and sub picture will appear together with same size of the screen. The picture of left side is primary and that of right side is sub. If you press PIP button one more time, sub picture will be disappeared.

- In the PIP mode, you can change primary and sub with PIP SWAP button.

- If you press PAGE UP/DOWN button, the location of sub picture is changed.

- If you press PIP SERVICE LIST button, you can see the list of services of sub picture. 
You can change the service of sub picture from the list.

NOTE : Changing services of sub picture could be limited by the condition of tuner connection or recording.

PVR (Personal Video Recorder) Function

- Recording

You can select a recording storage device with following sequence : 
Menu > Configuration > Recording Option > Record Device.
Default is set to ‘Hard Disk’.

  - Recording methods

There are 3 type recording methods.

(Instant Recording / Time Reserved Recording / Event Reserved Recording).

- Instant Recording : 
At anytime, you may press RECORD button to start your recording instantly.

- Time Reserved Recording :

        - In Timer Manager menu, you may set the time & program to record your desired service program. 
(Main Menu > Configuration > Timer Manager)

        - Press GREEN button to activate the new timer edit screen.

        - In the Timer Edit screen, you may choose start date/time, duration, service, mode, type (Recording/Play), Tuner (Auto/1/2) then simply press Yes button to reserve your recording schedule.  Please note that the minimum offset time of 3 minutes are required from the Start time & current time for appropriate recording process to take place.

- Event Reserved Recording :
In the EPG menu screen, you can choose the event you wish to reserve or record.

        - While watching the LIVE TV screen, press EPG button to access EPG menu screen.

        - Go to the event which you wish to reserve and view, then press OK.  The event will be reserved with BLUE play icon.  This BLUE play icon means that you want to just watch the event at the reserved time.

        - Press OK button one more time, then the event will be reserved with RED dot icon. This RED dot icon means that you want to record the event at the reserved time.

        - When you set an event for reserve and recording in EPG menu.  It automatically sets a Timer Event in Main Menu > Configuration > Timer Manager.

  - Recording Edit

Press REC button while recording to see the recording message window.

- Pause : Select Pause Recording then press OK to pause the current recording process.

- Duration : Set recording duration. Press Left/Right ARROW button to change recording duration.

- Stop Position : 
Set the finishing time of recording.

        - End of current event : finish recording at the end of current event

        - End of next event : finish recording at the end of next event.

        - Not Available : EPG is not available.

- Record Slot : When you are recording 2 services, you can set Primary / Secondary with Left/Right ARROW button.  Press OK button to go to the recording service.

  - Long Time recording

During long time recording process of 4GB(Giga Byte) or more, additional files may be created per every 4GB. (For example; aaa.ts, aaa.ts1, aaa.ts2… and so on).

You must remember not to erase any of duplicated file. These files are only able to view with your PC not with receiver (STB).

  - Pause during recording

- When PAUSE button is pressed during recording, only the live video is paused, but recording is continued at the selected recording device. 
(Menu > Configuration > Recording Option > Record Device)

- Press PAUSE button once again and event will resume from the pause time.

- During recording, press PLAY/TIMESHIFT button to show Play bar screen.

- While the Play bar is shown on your screen, you may use the LEFT/RIGHT ARROW button to move (forward & backward) freely within recorded time.

- If you press STOP button, it will go to LIVE and you may press PREV FILE button to view recorded file from the beginning.

- When recording 2 services at the same time, Press STOP button to see message window of current recording status / information. 
If you select one of the 2 recordings and press OK button, that recording service will be stopped. 
If you press STOP button during recording 1 service, the recording will be stopped.

NOTE : Dual Recording 
STB can record up to two different services simultaneously. Time shifting is also a recording, so Time shifting will be possible on one of the two recordings during dual recording.

- Time Shifting

You can select a storage device for temporary file of Time shifting with following sequence:

Menu > Configuration > Recording Option > TimeShift Device.

Default storage device is set to ‘Hard Disk(SATA)’

- If pressed PAUSE button during Time shift, live video is paused but temporary recording for time shift is continued at the selected storage device.

- Press PAUSE button once again, then the event will resume from the paused time.

- While watching live TV, press PLAY/TIMESHIFT button to show the play bar on your screen.

- When the play bar is displayed on your screen, you may use the LEFT/RIGHT ARROW buttons to move freely through recorded times.

- If you press STOP button while time-shifting, screen will be turned to live TV channel.  You can also use PREV FILE button to move to a start location of Time-shifted file.

- Playback (Play List)

You can playback the files in the Playlist.

In the Playlist, you can check and playback multimedia files of movie, music, and image.  With LEFT/RIGHT ARROW button, go to movie, music, and image category and check & palyback files in the category. Press RIGHT ARROW button once to go to MP3 Player list and press RIGHT ARROW button one more time to go to Image Viewer.

  - Play List

- Select Device : Press PLAYLIST button one more time in the Playlist mode to see “Select Device” window, and select the device which has the file you want to play.

NOTE : “Select Device” window shows devices which are currently connected to the STB.

- Sorting : If you press YELLOW button, you can sort the files by Time / Name / Size.

- File Option : If you press BLUE button, You can delete or move files, make a folder, rename in File Option.  You can select multiple files together and delete or move all of them at once.

  - MP3 Player

- If you press RIGHT ARROW button in Playlist, you can go to MP3 Player menu.

- If you press RECALL button, you can enjoy music with Shuffle playback and repeat.

- You can use the same ‘Sorting’ and ‘File Option’ features same as in the Playlist menu.

  - Image Viewer

- If you press RIGHT ARROW button in MP3 Player, you can go to Image Viewer menu.

- If you press RED button or OK button, you can start slide show of image files.

- If you press GREEN button, you can adjust Slide Time, Repetition, Title, Down-scale.

- You can use the same ‘Sorting’ and ‘File Option’ features same as in the Playlist menu.

- Bookmark

- When Play bar is displayed, you may move to desired time and book mark it by pressing the RED button.   Bookmark(s) are indicated with Green line on the play bar. Also, you may press RED button to activate play bar to mark your bookmark(s).

- When the play bar is on, User can move / jump between the bookmarks by pressing the GREEN button.

- If you wish to delete any Bookmarks, go to that bookmark by pressing green button or arrow key, then press RED button to delete the current bookmarks.

- Trick mode

- User can change the speed of a fast forward play with FF(Fast Forward) button. Press FF button to change the speed to x2, x3, x4, x5.  If you once again press FF button in its x5 mode, it returns to normal(x1) speed play.

- You can also change rewind speed with REWIND button. Press REWIND button to change the speed to x2, x3, x4, x5.  If you press REWIND button again in its x5 mode, it returns to normal speed.

- You may press PAUSE button at any time to pause a pre-recorded event. Press PAUSE button once again to resume play of the recorded event.

Guide of Main Menu

To display the menu, press MENU button at any time. You can select the sub menus by using the ARROW buttons. 
The selected sub menu becomes highlighted.  After selecting the sub menu you want to access, press OK button. If you want to return to the previous menu, press the MENU button. And if you want to exit from the menu, press the EXIT button.

- System Tools

  - Storage Manager

The items in this menu allow you to access and control the storage devices that you want.

- Current Device : Select the storage device you want to access with the ARROW/OK buttons.

- Status : You can see the information of current connected devices, such as ‘Mounted’, ‘Not Available’

- File System : It shows the file system of current device. You can also select desired file system that you want when you format the device.

NOTE : You must select FAT32 file system, if you want to access USB storage devices in Windows

- Total : Displays total size of current device.

- Free : Displays free size of current device.

- Format : If you press OK button to format current device, the device will be formatted with above file system.

NOTE : When file system is ‘Unknown’, the device will be formatted with ‘Journaled’.

- Play List : Press OK button to move to ‘Play List’ menu directly.

  - Timer Manager

Insert a new timer entry or modify the existing timer entry.

- To add new timer entry : Press GREEN button. Timer Edit window will popup. You can set the specific start date, time, duration and service for its reservation. And you can choose one of Timer Modes as 'Once' or 'Daily' or 'Weekly'. You can choose timer operation type as ‘Recording’ or just to 'Play'.

        - If you choose 'Recording', it will start recording at that time.

        - If you choose 'Play', it will change and tune to the service that you wish to watch.

- To modify existing timer entry : Choose the timer entry which you wish to modify and press OK button.

- To delete existing timer entry : Choose the timer entry that you want to delete and press RED button.

NOTE : If you reserve one or more event through the EPG menu, the reserved event(s) will be added to Timer Manager automatically.

  - Service List manager

Service List Manager menu will be appeared when press OK button.

You can select Edit Mode by press YELLOW button.

- Lock Services : All lists will be shown on left side of window, right side will show the list of service to be locked. By using ARROW and OK button, you may move the chosen service to right side window to lock that service.

- Move Services : All Lists will be shown on left side of window, Lists for moving will be shown on right side window. Move the service to right side window by using ARROW and OK button, then right side window service will be moved to specified location when the desired location is selected from the left window.

- Delete Services : All Lists will be shown on left side of window.  By using ARROW and OK button you may select services to be deleted.  And press GREEN button to delete the selected service.

- Skip Services : All services will be shown on left side of window, right side will only show the services that are chosen to be skipped.  By using ARROW and OK button you may move the selected service from left to right side  to skip them.

- Set Favorite Services : Use the ARROW and OK button to select your desired favorite group. Once, favorite group is chosen, left side window will show all service list and right side window will only show the selected services of the favorite group chosen.  By using ARROW and OK buttons, you may ADD the desired services to a favorite group or DELETE any from the favorite group.

- Edit Services : All services list will be shown on left side of window. Move the highlighted bar to the service which you want to edit its name and press OK button. Then you can see the virtual keyboard. Using ARROW and OK buttons, you can edit the name with keyboard.

  - Data Transfer

When the data transfer task is in process, the Front USB slot is set to a default device slot.  But, if no USB device is connected on a front USB slot, then the Rear USB slot is set as a device to be used for the data transfer process.

NOTE : If no USB device is connected on either two (Front & Rear) USB slots, then a Menu item will not be available.

- Transfer all System data to USB storage : If you want to transfer and use BOTH of the current system parameters and service data in the future, this menu will allow you to store both data to your USB device. Press OK button to store current data to external USB storage.

- Transfer Service data to USB storage : If you want to transfer and use ONLY the service data in the future, this menu allows you to store current service data. Press OK button to store the current service data to your external USB storage.

- Data download from USB storage device : This menu allows you to download the stored data from the external USB storage to your STB. Press OK button to download data.

- Configuration

  - Recording Option

- Confirming message for ‘stopping’ your Recording process :

        - Set 'On' : When you press STOP button while recording, then a confirm window is displayed.

        - Set 'Off' : When you press STOP button while recording, STB will stop the recording process immediately / Instantly with no extra confirming message asked.

- Extra Event Recording : 
You can adjust extra recording time. (1 Min/2 Min/3 Min/4 Min/5 Min/10 Min/15 Min/off )
If you set an extra recording time by using ARROW and OK button, pre-reserved recording time will be added on a ‘Start’ and ‘End’ time of that event being recorded.
This option only affects the actual work the Timer. But, when you reserve a service recording in the Timer Manager menu, this option has no affection.

- Time-Shift : 
You can adjust the time. (30 Min/60 Min/90 Min/120 Min)
In this case, time shifting function works automatically up to the limit of time that you set, as long as the Time-Shift storage device has enough memory space.
If you set this option to ‘OFF’ status, then the time shifting function never works.

- Time-Shift Device : 
You can choose and set a Time-Shift Device you want, such as Hard Disk / USB1(Front) / USB2(Rear).

- Record Device : 
You can also set a Record Device which you want to use, such as Hard Disk / USB1(Front) / USB2(Rear).  Recorded files are stored in that device you set.

  - Parental Control

User’s access rights to a service and programs are controlled by a 4-digit secret code that is defined by the user. Whenever you attempt to access the parental control menu, a pop-up window will ask you to input a PIN code. (If necessary, you can change it.)

NOTE : The default PIN code is ‘0000’

- Censorship : Set the parental guidance rating of highlighted censorship classification. The parental level is given as age-based numbers.

- Change Pin code : To change your PIN code, input the new PIN code using  buttons. To verify the new PIN code, input the new PIN code again.

- System : Set the access rights to system menu.

- Installation : Set the access rights to Installation menu.

- Configuration : Set the access rights to Configuration menu.

- Edit Service : Set the access rights to Edit menu.

  - UI (User Interface) Setting

- Info Box position : Set a position of information window.

- Info Box Display Time : Set the time duration of information window being displayed on the screen after changing services.

- Volume Bar Display Time : Set the time duration of volume bar being displayed on the screen after changing audio volumes.

- EPG Time Range : You can set the time range which is displayed at the same time in the EPG window.

- Zapping Mode : You can set the zapping mode.

        - Black screen : Display the black screen when channel is changed between services.

        - Freeze : Display the last still picture when changing services.

- Front Display Scroll : You can set VFD Display Scroll.

        - On : Continually scroll service name, if digit of the service name is over 12 characters.

        - Off : Scroll service name once, if digit of the service name is over 12 characters.

- LED Lighting Time : You can adjust the lighting time of front LED.

- LED Brightness : You can adjust brightness of front LED with 4 steps. By setting ‘off’ this option, will turn OFF the front LED lighting.

  - Time Setting

- Time Setting : To set the current time, you can use two modes; Auto and Manual.

        - Auto Time Setting
Local Offset : Enter the offset value by using the standardized information of current service area.
Daylight Saving : If you want to apply daylight saving, select the counter by using ARROW buttons.

        - Manual Time Setting
Date : Enter the calendar date by using ARROW buttons then press OK button to finish. 
Time : Enter the time by using the NUMERIC buttons.

- Clock Mode : Select the type of clock display(12 Hours or 24 Hours) using ARROW buttons.

- Wake Up Mode : Enter the time for the receiver to automatically power ON. And you can choose one of Wake Up Mode as ‘off’ or ‘Once’ or ‘Daily’ or ‘Weekly’.

        - Wake Up Date : Select the date when STB is turn on. Press OK button to display calendar.

        - Wake Up Days : Select a day of the week when STB is turn on.

        - Wake Up Time : Enter the wake up time of STB using NUMERIC buttons.

        - Wake Up Service : Select the service when STB is turn on. Press OK button to display service list.

- Sleep Mode : Enter the time for the receiver to automatically switch OFF and go to standby mode. And you can choose one of Wake Up Mode as 'off' or 'Once' or 'Daily' or 'Weekly'.

        - Sleep Date : Select the date when STB is turn off. Press OK button to display calendar.

        - Sleep Days : Select a day of the week when STB is turn off.

        - Sleep Time : Enter the turn-off time of STB using NUMERIC buttons.

  - Language Setting

- Menu Language : Select the desired menu language by using the ARROW buttons.

NOTE : The Kind of languages can be changed depending on the country sold. Available languages are subject to change without prior notice.

- Audio Language : Select the default language for audio when changing services.  If no other language is provided, then the default language of current will be automatically selected.

- Subtitle Language : Select the default language for subtitle when changing service.

  - A/V Output Setting

- TV Type : Select the TV types.(PAL/NTSC/Auto) In Auto mode, the STB is automatically selected as NTSC or PAL according to the service played.

- TV Aspect Ratio : Select the aspect ratio of TV which is connected to STB.(4:3/16:9). This menu must be set first to select Display Format function.

- Display Resolution : Select  the Display Resolution of screen by using ARROW or OK button. You can also change the resolution with Resolution button in RCU. Each time you press the Resolution button, the resolution changes in the following sequence: 
576i > 576p > 720p > 1080i

NOTE : Please note that your TV cannot display everything according to Display Resolution. If you set the Display Resolution as SD(576i), your TV cannot display anything when TV output settings is Component Video(YPbPr) in your TV setting menu. If you set the Display Resolution as HD(more than 576p), your TV cannot display anything when TV output settings are SCART or Composite Video in your TV setting menu. In case of HDMI, your TV can display all of resolution that your TV can support. But it is also possible that your TV may not display anything with 576i, because some of HDTV does not support 576i.

- Display Format : 
In case of 4:3 ratio TV set, You can select Letter Box or Pan&Scan. In case of 16:9 ratio TV set, You can select Pillar Box or Full Screen.

        - 16:9 Display format on 4:3 TV set 
Letter Box : You can see  the full screen of 16:9, but  top and bottom edges of your TV screen display black horizontal Pillars. 
Pan&Scan : The picture is displayed in full on your 4:3 TV screen, but left and right sides of the original picture cannot be displayed.

        - 4:3 Display format on 16:9 TV set 
Pillar Box : You can see the full screen of 4:3, but left and right sides of your TV screen display black vertical Pillars. 4:3 
Full Screen : The picture is displayed in full on your 16:9 TV screen, but left and right sides of the original picture is displayed with increasing the screen from left and right. Because of artificial increase, TV screen will be distorted.

- Video Output Mode : According to Display Resolution, you can select the Video Output Mode.

        - In case of More than 576p(HD) : The ‘RGB’ output will be disabled automatically. You can select Video Output Mode (CVBS, YPbPr, YC).

        - In case of 576i(SD) : The ‘YPbPr’ output will be disabled automatically. You can select Video Output Mode (CVBS, RGB, YC).

- Sound Mode : Set the audio mode output among the RCA jack, optical SPDIF and HDMI.(Stereo/Mono/Left/Right).

- Installation

  - Dish Setting

Select the antenna and LNB settings for service search. The values that are set in this menu will be available for selection in other service searching menus.

- Satellite : Select the satellite which you want to search the service.

        - Press the LEFT/RIGHT ARROW button to select the satellite.

        - If you press OK button, satellite list will be displayed.

        - Select the desired satellite name to search.

        - If the desired satellite name is not listed then select User Defined.

- Tuner Connection : You can set connection type between Tuner and LNB.

        - Separate : Set the connection type option to ‘Separate’, if the each tuners are connected to a different LNBs (LNB IN_1 / LNB IN_2) individually / independently.
This Separate connection is used, when each two tuners are connected to different LNBs.  Due the independent & separate connections between two Tuners & LNBs, User can watch all the services scanned by one tuner(1), while the other tuner(2) is in recording process at the same time.

        - Loop-Through : Set the connection type option to ‘Loop-Through’, if you have connected the LNB OUT_1 and LNB IN_2 with a loop-through cable. In this case, you would have some limitations in using some features such as dual recording. 
This connection is used when the Tuner(1) is connected with LNB output, and the Loop-through output of the Tuner(1) is connected with input of the Tuner(2). This is the way to use & activate both tuners when you have only 1 LNB with your dish antenna.  However, this will limit the possible tuning range (Satellite & Polarization) of the 2nd tuner, while the 1st tuner is being used for its recording process (because the input signal of 2nd tuner is dependent of the signal which the 1st tuner is tuned to).

NOTE : User should make the appropriate connection by choosing the right tuner connections between the  Loop-Through and Separate connections.  Due to the difference of these two connections, wrong LNB and Tuner connection may cause the lack of signal reception.  We strongly recommend the professional service personnel to make this installation and connections.

- Tuner : Select tuner which you want to set (Tuner 1/ Tuner 2). If you set ‘Loop-Through’ on the menu(Installation-Dish Setting-Tuner Connection), this menu(Tuner) will be disabled automatically.

- Frequency : Select frequency what you want to check the signal.

- LNB Power : Select the LNB power.

- LNB Type : Select the LNB type.

- LNB Frequency : Select the L.O. frequency that is set to antenna.

        - Use the LEFT/RIGHT ARROW buttons to select the LNB frequency.

        - If the required LNB frequency is not listed, then enter the frequency manually using the NUMERIC buttons.

        - When you select Universal in LNB type, both 9750 and 10600 are supported at the same time. And LNB 22KHz setting is disabled.

- LNB 22KHz : When you use a dual LNB or two antennas connected to a 22 KHz tone switch box, make 22 KHz tone switch enable or disable to select LNB or antenna.

- DiSEqC SW : If you use DiSEqC 1.0 or DiSEqC 1.1 switch, select one of the DiSEqC inputs.

- Service Search : Press OK button to move to Search menu directly.

  - Positioner Setting

- Satellite : Select the satellite which you want to search the Service.

        - Press the LEFT/RIGHT ARROW button to select the satellite.

        - If you press OK button, satellite list will be displayed.

        - Select the wanted satellite name.

        - If the desired satellite name is not listed then select User Defined.

- Tuner : Select tuner that you want to set (Tuner 1/ Tuner 2). If you set ‘Loop-Through’ on the menu(Installation-Dish Setting-Tuner Connection), this menu(Tuner) will be disabled automatically.

- Frequency : Select frequency which you want to check the signal.

- Positioner : Select the positioner.

        - None : (No Positioner)

        - Using DiSEqC 1.2 : 
Move : To move the dish, press LEFT/RIGHT button. 
Fine Move : To move the dish in detail, press LEFT/RIGHT ARROW button. 
Step : Set to positioner moving steps as 1, 2, 3, 4 
Positioner Command : To use various positioner command, press OK button. Then, available positioner commands will appear.

        - Using USALS : 
Move : To move the dish, press LEFT/RIGHT button. 
Fine Move : To move the dish in detail, press LEFT/RIGHT ARROW button. 
Step : Set to positioner moving steps as 1, 2, 3, 4 
Dish Longitude : Enter the longitude using the NUMERIC buttons. 
Dish Latitude : Enter the latitude using the NUMERIC buttons. 
Go To : Press OK button to rotate the dish to the configured position.

- Dish Setting : Press OK button to move to Dish Setting menu directly.

- Service Search : Press OK button to move to Service Search menu directly.

  - Service Search

You can select the following search mode.

- Auto Mode :

        - Satellite : Press OK button to select the target satellite for search.

        - Tuner : Select tuner what you want to set (Tuner 1/ Tuner 2). If you set ‘Loop-Through’ on the menu(Installation-Dish Setting-Tuner Connection), this menu(Tuner) will be disabled automatically.Search Type : Select the search type.

        - Network Search : You can select Off or On. When you select ‘On’, you can find more transponders using the home network. As it refers to NIT during searching, if there is the frequency information of other transponder, it searches the other transponder besides the transponder that the user inputs.

        - Dish Setting : Press OK button to move to Dish Setting menu directly.

        - Positioner Setting : Press OK button to move to Positioner Setting menu directly.

        - Start Search : Press OK button to start search.

- Manual Search Mode :

        - Satellite : Press OK button to select the target satellite for search.

        - Tuner : Select tuner what you want to set (Tuner 1/ Tuner 2). If you set ‘Loop-Through’ on the menu(Installation-Dish Setting-Tuner Connection), this menu(Tuner) will be disabled automatically.

        - Frequency : Select the frequency from the list to search.

        - Symbol rate : Enter the symbol rate using the NUMERIC buttons.

        - Polarity : Select the polarity. (Vertical/Horizontal)

        - Search Type : Select the search type.

        - Network Search : You can select Off or On. When you select ‘On’, you can find more transponders using the home network. As it refers to NIT during searching, if there is the frequency information of other transponder, it searches the other transponder besides the transponder that the user inputs.

        - Dish Setting : Press OK button to move to Dish Setting menu directly.

        - Start Search : Press OK button to start search

- Blind Search Mode :

        - Satellite : Press OK button to select multiple satellites.

        - Tuner : Select tuner what you want to set (Tuner 1/ Tuner 2). If you set ‘Loop-Through’ on the menu(Installation-Dish Setting-Tuner Connection), this menu(Tuner) will be disabled automatically.

        - Frequency : Set Auto to search whole frequency, Set Manual to search only desired frequency.

        - Polarity : Select the polarity. (All Polarity/Vertical/Horizontal)

        - Search Type : Select the search type.

        - Dish Setting : Press OK button to move to Dish Setting menu directly.

        - Start Search : Press OK button to start search.

- Advanced Search Mode :

        - Satellite : Press OK button to select the target satellite for search.

        - Tuner : Select tuner what you want to set (Tuner 1/ Tuner 2). If you set ‘Loop-Through’ on the menu(Installation-Dish Setting-Tuner Connection), this menu(Tuner) will be disabled automatically.

        - Frequency : Select the frequency from the list to search.

        - Symbol rate : Enter the symbol rate by using the NUMERIC buttons.

        - Polarity : Select the polarity. (Vertical/Horizontal)

        - Video PID : Enter the video PID using the NUMERIC buttons.

        - Audio PID : Enter the video PID using the NUMERIC buttons.

        - PCR PID : Enter the video PID using the NUMERIC buttons.

        - Start Search : Press OK button to start search.

  - Network Setting

To use Network, you have to prepare router. When STB and PC are connected via network, You can control the file of STB storage device such as SATA HDD, USB storage device.

NOTE : If you use DHCP function of router, you can set easily network configuration.

- DHCP : You can select On/Off of DHCP to get the all configuration from the router.

        - If you select ‘On’ : You can get the all configuration from router and set automatically. In this case, the rest item(IP Address, Subnet Mask, Gateway, First DNS, Second DNS) are set automatically and you don’t have to configure them manually.

        - If you select ‘Off’ : You have to input the IP address manually.

- IP Address, Subnet Mask, Gateway, First DNS, Second DNS : You can input the address with the OK button, NUMERIC buttons and the LEFT/RIGHT buttons. You can move to the next item of Subnet Mast with the DOWN button and you can configure the following items in the same way.

- Firmware Upgrade Server : This feature is not supported for the time being.  It will be informed to the Users when this feature would be available in the future.

- MAC Address : This will display the MAC address of the Ethernet interface but you can ‘t change it.

- Control the file via network on your PC.

        - Check IP Address of STB on Network Setting menu.

        - Press Enter button on your PC, after writing IP Address on the web browser address.  
Ex.) \\168.158.10.146\storage

        - You can see the folder name of HDD, USB1 and USB2 in the Storage folder. 
HDD : SATA HDD (internal HDD or external-SATA) 
USB1 : Front USB Storage Device 
USB2 : Rear USB Storage Device

  - System Recovery

- System restore to factory default : This menu allows you to restore the factory set values in case the user has encountered some problems after changing any new parameters of service data and others which may be in error. Press OK button to erase all services and restore default setting.

- System restore to stored position : This menu allows you to restore the stored values including service data and system parameters. Press OK button to restore all data.

- Store system data : If you want to use system parameters and service data in the future, this menu allows you to store current state. Press OK button to store current state.

  - System Information

This menu displays general information about the hardware and software version of your receiver.

- Utilities

  - Calculator

To use a calculator, press OK button.

  - Calendar

To display calendar, press OK button. Utilize ARROW buttons to choose the date. If you press PAGE UP/DOWN button, you can see past/next month of calendar.

  - CAS (Conditional Access System)

- Smart Card Slot

        - Conax smart card menu 
To watch scrambled services, you need to have a appropriate Conax smart card from the service providers. Insert a valid smart card into smart card slot. The message of ‘Smart card Initializing…’ will appear on the screen. After message disappears, you can watch the service you want.

        - Smart card information 
You can view the current status of smart card. Select the slot what you want to view using ARROW buttons. And press OK button.

- CAM Initializing 
To watch scrambled services, you need to have a Common Interface Conditional Access Module(CAM) and a appropriate smart card from the providers. Insert CAM together with a valid smart card into CI slot. The message of ‘CI Initializing…’ will appear on the screen. After message disappears, you can watch the service you want.

- CAM information 
You can view the current status of CAM. Select the slot what you want to view using ARROW buttons. And press OK button. If the CAM is available, you can view information about each slot.

NOTE : The displayed information of each CAMs may be different depending on CAM.

Troubleshooting

| Problem | Solution |
| --- | --- |
| Does not display any message on the front panel. | Check the main power cable and check that it is plugged into a suitable power outlet. Check the STB main power switch ‘ON’ at the rear of the STB. |
| No Picture | See ‘Does not display any message on the front panel’ above. To match the STB system with your TV system(PAL/NTSC), press V.Format button until a picture is displayed. Check the video output port is firmly connected to the TV or VCR. If you are using the RF output, check that the RF lead is connected firmly to the STB and TV/VCR. Check that you have selected the correct channel or Video Output on your TV. If you are using the RF Output, check that you have correctly tuned the UHF channel of the STB or TV. Check the brightness level of the TV. Check the resolution that your TV supports, and set the proper resolution with RCU Resolution button to obtain a picture. |
| Poor picture quality | See ‘No Picture’ above. Check the signal level, if this is low then tries adjusting the alignment of your dish. |
| No Sound | See ‘No Picture’ above. Check the volume level of the TV and STB. Check the Mute status of the TV and STB. |
| Remote Control does not operate | Point remote control directly towards the STB. Check and replace batteries. |
| No or Bad Signal | Check the LNB ; Replace LNB if necessary. Check the cable from the LNB. Check the position of the dish; realign dish if necessary. If you are using a DiSEqC 1.0 switch, check that you have connected the LNBs to the correct connections on the switch. Check the ‘Signal Level’ and the ‘Signal Quality’. |

Specifications

| Tuner & Channel Decoder |
| --- |
| Input Connector Loop through out Frequency Range Input Impedance Signal Level LNB Power 22KHz Tone DISEqC Control Demodulation Input Symbol Rate FEC Decoder | F-type, IEC 169-24, Female F-type, IEC 169-24, Female 950MHz ~ 2150MHz 75Ω, unbalanced -65 to -25dBm 13/18VDC, max.400mA (22±2)KHz, (0.6±0.2)V V1.0/1.2/USALS Compatible QPSK / 8PSK 2 ~ 45 Ms/s(QPSK of DVB-S) 2 ~ 45 Ms/s(QPSK of DVB-S2) 2 ~ 37 Ms/s(8PSK of DVB-S2) 1/2, 2/3, 3/4, 5/6 and 7/8 with Constraint Length K=7(DVB-S) 1/2, 3/5, 2/3, 3/4, 4/5, 5/6, 8/9 and 9/10 (DVB-S2) |
| MPEG Transport Stream A/V Decoding |
| Transport Stream Profile Level Input Rate Video Formats Video Resolution Audio Decoding Audio Mode Sampling Rate | H.264(MPEG-4 part 10, MPEG-4/AVC and H26L) MPEG-II ISO/IEC 13818-2/11172-2 MPEG-4/AVC MP@L4, MPEG-II MP@HL Max. 15Mbit/s 4:3 Letter Box, 4:3 PanScan, 16 : 9 720 x 576i, 720 x 576p, 720 x 480i, 720 x 480p 1280 x 720p, 1920 x 1080i Dolby AAC, AC-3, MPEG-1 Layer 1,2 and 3 Stereo/Joint stereo/Mono, Dolby AC-3 32KHz, 44.1KHz and 48KHz(According to input) |
| Main System |
| Main Processor Memory | STi chipset Flash-ROM : 32 Mbyte SDRAM : 192 Mbytes EEPROM : 128 bytes |
| Audio / Video & Data IN/OUT |
| TV SCART VCR SCART RCA Component HDMI OPTIC RS-232C USB e-SATA | RGB, Y/C, CVBS Video, Audio L, R Output CVBS Video, Audio L, R Output RGB Video input, CVBS Video, Audio L, R Input CVBS Video Output, Audio L, R Output YPbPr Video Output Video & Audio Output AC-3 Dolby Digital (SPDIF) 9 pin D-SUB (Male) type, Transfer rate 115Kbps USB 2.0 Host Support (Front & Rear) External SATA HDD Support |

| RF Modulator |
| --- |
| RF Connector Frequency Output Channel TV Standard Preset Channel | 75Ω, IEC 169-2, Male/Female 470 ~ 860MHz CH 21 ~ 69 for the Remodulator PAL G/I/K Selectable by Menu CH 36 (or TBD) Software changeable by Menu |
| Front Panel |
| Slot Display Buttons | 1 USB 2.0 Host port 2 Common interface & 1 Smart Card Slot VFD(Vacuum Fluorescent Display) - 12Digit 5 Buttons(Standby, CH UP/DOWN, Volume UP/DOWN) |
| Power Supply |
| Input Voltage Type Power Consumption Standby Power Protection | AC 100 ~ 250V, 50/60Hz SMPS Max. 60W Max. 1W Separate Internal Fuse & Lighting protection |
| Physical Specification |
| Size (W x H x D) Weight (Net) Operating Temp. Storage Temp. | 340mm X 60mm X 230mm 2.0 Kg 0°C ~ +45°C -10°C ~ +70°C |

Code Table for Universal Remote Control Unit

- Key Table

| No | KEY NAME | TV | DVD | VCR |
| --- | --- | --- | --- | --- |
| 1 |  |  |  |  |
| 2 |  | V |  |  |
| 3 |  |  | V | V |
| 4 |  | V | V | V |
| 5 |  | V |  |  |
| 6 | V.Format |  |  |  |
| 7 | SLEEP |  |  |  |
| 8 | TV/RAD, Source | V |  |  |
| 9 | Resolution |  |  |  |
| 10 |  |  | V | V |
| 11 |  |  | V | V |
| 12 |  |  | V | V |
| 13 |  |  | V |  |
| 14 |  |  | V |  |
| 15 |  |  | V | V |
| 16 |  |  | V | V |
| 17 |  |  | V | V |
| 18 |  |  |  |  |
| 19 |  | V |  |  |
| 20 |  | V |  |  |
| 21 |  | V |  |  |
| 22 |  | V |  |  |
| 23 | INFO |  |  |  |
| 24 | RECALL |  |  |  |
| 25 | MENU | V | V |  |
| 26 | EXIT | V | V |  |
| 27 |  | V | V |  |
| 28 |  | V | V |  |
| 29 |  | V | V |  |
| 30 |  | V | V |  |
| 31 | OK | V | V |  |
| 32 |  |  |  |  |
| 33 | FAV |  |  |  |
| 34 |  |  |  |  |

| No | KEY NAME | TV | DVD | VCR |
| --- | --- | --- | --- | --- |
| 35 | VOL + | V |  |  |
| 36 | VOL - | V |  |  |
| 37 | CH + | V |  | V |
| 38 | CH - | V |  | V |
| 39 | EPG |  |  |  |
| 40 |  |  |  |  |
| 41 |  |  |  |  |
| 42 |  |  |  |  |
| 43 |  |  |  |  |
| 44 | 0 | V | V | V |
| 45 | 1 | V | V | V |
| 46 | 2 | V | V | V |
| 47 | 3 | V | V | V |
| 48 | 4 | V | V | V |
| 49 | 5 | V | V | V |
| 50 | 6 | V | V | V |
| 51 | 7 | V | V | V |
| 52 | 8 | V | V | V |
| 53 | 9 | V | V | V |
| 54 |  |  |  |  |
| 55 |  |  |  |  |
| 56 | REV1 |  |  |  |
| 57 | REV2 |  |  |  |
| 58 | REV3 |  |  |  |
| 59 | REV4 |  |  |  |
| 60 | REV5 |  |  |  |
| 61 | REV6 |  |  |  |

- TV Brands

| TV Brands | Code |
| --- | --- |
| ADMIRAL | 050 | 134 |  |  |  |
| AKAI | 093 | 049 | 123 |  |  |
| ALBA | 068 |  |  |  |  |
| ALBIRAL | 116 |  |  |  |  |
| ALCATEL | 022 |  |  |  |  |
| AMSTRAD | 158 | 021 |  |  |  |
| ANAM | 155 | 156 | 157 |  |  |
| ARC EN CIEL | 028 | 039 | 043 | 145 | 081 |
| ARISTONA | 099 | 049 | 050 | 019 | 142 |
|  | 149 | 078 |  |  |  |
| ARTHUR MARTIN | 053 | 139 | 117 | 120 | 122 |
|  | 123 | 125 | 128 |  |  |
| ASA | 050 | 055 | 057 | 113 | 134 |
| ATLANTIC | 099 | 111 |  |  |  |
| AUDIOSONIC | 054 |  |  |  |  |
| AUSIND | 053 |  |  |  |  |
| AUTOVOX | 099 | 144 | 055 | 019 | 057 |
|  | 069 |  |  |  |  |
| BAIRD | 083 |  |  |  |  |
| BASICLINE | 006 |  |  |  |  |
| BAUR | 011 |  |  |  |  |
| BEKO | 023 | 049 |  |  |  |
| BLAUPUNKT | 094 | 100 | 102 | 111 | 114 |
| BRANDT | 028 | 039 | 040 | 043 | 145 |
|  | 081 |  |  |  |  |
| BRION VEGA | 050 |  |  |  |  |
| BRUNS | 048 | 050 |  |  |  |
| BSR | 059 | 110 | 132 |  |  |
| BUSH | 033 | 068 | 124 | 074 |  |
| CENTURY | 098 | 101 | 050 | 079 | 136 |
| CGE | 016 | 101 | 124 | 079 | 132 |
|  | 136 |  |  |  |  |
| CIHAN | 065 |  |  |  |  |
| CLARIVOX | 048 | 116 |  |  |  |
| CONDOR | 099 | 111 |  |  |  |
| CONTEC | 087 |  |  |  |  |
| CONTINENTAL EDITION | 028 | 039 | 040 | 043 | 145 |
|  | 081 |  |  |  |  |
| CROSLEY | 101 | 050 | 109 |  |  |
| CROWN | 147 |  |  |  |  |
| CTC CLATRONIC | 046 |  |  |  |  |

| TV Brands | Code |
| --- | --- |
| DAEWOO | 089 |  |  |  |  |
| DECCA | 099 | 060 | 063 | 115 | 118 |
| DEGRAAF | 036 |  |  |  |  |
| DIXI | 049 | 090 |  |  |  |
| DRYNATRON | 049 |  |  |  |  |
| DUAL | 099 | 141 |  |  |  |
| DUAL-TEC | 096 | 099 | 132 |  |  |
| DUMONT | 046 | 050 | 057 | 073 |  |
| ELBE |  | 016 | 116 |  |  |
| ELBIT | 065 |  |  |  |  |
| ELCIT | 046 | 097 | 103 | 050 | 109 |
|  | 127 | 132 |  |  |  |
| ELMAN | 046 | 132 |  |  |  |
| ELTA | 090 |  |  |  |  |
| EMERSON | 158 | 098 | 050 |  |  |
| ERRES | 049 | 142 |  |  |  |
| EUROPHON | 098 | 046 | 097 | 099 | 051 |
|  | 115 | 132 |  |  |  |
| FERGUSON | 146 | 040 | 041 | 150 | 057 |
|  | 061 | 116 | 149 |  |  |
| FIDELITY | 099 | 149 |  |  |  |
| FINLUX | 034 | 046 | 053 | 055 | 057 |
|  | 109 | 113 | 073 | 074 | 079 |
| FISHER | 015 | 048 | 050 | 052 | 109 |
|  | 136 |  |  |  |  |
| FORGESTONE | 149 |  |  |  |  |
| FORMENTI | 099 | 053 | 109 | 111 | 125 |
| FORTRESS | 137 |  |  |  |  |
| FRABA | 075 |  |  |  |  |
| FRONTECH | 054 |  |  |  |  |
| FUJITSU | 025 |  |  |  |  |
| FUNAI | 054 | 059 |  |  |  |
| GBC | 109 | 132 |  |  |  |
| GEC | 099 | 060 | 109 | 115 | 134 |
|  | 088 |  |  |  |  |
| GELOSO | 103 | 109 | 132 | 134 | 090 |
| GOLDSTAR | 092 | 003 | 017 | 099 | 049 |
|  | 075 | 076 | 077 | 090 | 152 |
| GOODMANS | 033 | 049 | 060 | 077 |  |
| GORENJE | 066 | 136 |  |  |  |
| GREATZ | 001 | 058 | 109 | 122 | 123 |
|  | 128 | 129 | 130 | 134 |  |

| TV Brands | Code |
| --- | --- |
| GRANADA | 033 | 099 | 049 | 058 | 060 |
|  | 142 | 115 | 125 | 134 |  |
| GRUNDIG | 094 | 100 | 057 | 058 | 108 |
|  | 112 | 114 | 082 |  |  |
| HANSEATIC | 033 | 047 | 099 | 049 | 109 |
|  | 139 | 111 |  |  |  |
| HANTAREX | 097 |  |  |  |  |
| HEMMERMANN | 127 |  |  |  |  |
| HIFIVOX | 028 | 039 | 043 | 145 | 081 |
| HINARI | 158 | 033 | 045 | 143 | 090 |
| HITACHI | 014 | 033 | 034 | 036 | 099 |
|  | 145 | 056 | 109 | 139 | 110 |
|  | 067 | 117 | 132 | 134 | 084 |
|  | 091 | 081 | 088 |  |  |
| HYPER | 093 | 099 |  |  |  |
| IMPERIAL | 016 | 101 | 124 | 079 | 132 |
|  | 133 |  |  |  |  |
| INGELEN | 001 | 058 | 109 | 122 | 128 |
|  | 129 | 130 | 134 |  |  |
| INKEL | 000 |  |  |  |  |
| INNO HIT | 093 | 098 | 097 | 099 | 143 |
|  | 077 | 090 |  |  |  |
| INTERFUNK | 047 | 049 | 050 | 145 | 058 |
|  | 109 | 142 | 123 | 128 | 129 |
|  | 091 |  |  |  |  |
| IRRADIO | 093 | 143 | 053 | 077 | 090 |
| ITT | 001 | 140 | 058 | 105 | 109 |
|  | 122 | 123 | 128 | 148 | 129 |
|  | 130 | 134 | 135 | 083 | 089 |
| JVC | 033 | 154 |  |  |  |
| KTV | 099 |  |  |  |  |
| KAISUI | 006 |  |  |  |  |
| KARCHER | 006 |  |  |  |  |
| KENDO | 098 |  |  |  |  |
| KENNEDY | 144 | 019 | 109 |  |  |
| KORTING | 050 | 059 | 111 |  |  |
| KRIESLER | 099 | 049 | 050 | 019 | 142 |
|  | 149 | 078 |  |  |  |
| LENOIR | 099 |  |  |  |  |
| LOEWE OPTA | 008 | 097 | 047 | 049 | 050 |
|  | 115 | 072 |  |  |  |
| LOGIK | 118 | 149 |  |  |  |

| TV Brands | Code |
| --- | --- |
| LUMA | 049 | 120 | 134 |  |  |
| LUXOR | 058 | 139 | 117 | 120 | 123 |
|  | 129 | 135 | 083 |  |  |
| McMICHAEL | 088 |  |  |  |  |
| MEMOREX | 090 |  |  |  |  |
| MAGNAFON | 046 | 097 | 099 | 051 | 053 |
|  | 115 |  |  |  |  |
| MARANTZ | 049 |  |  |  |  |
| MATSUI | 158 | 099 | 106 | 060 | 118 |
|  | 068 | 134 | 090 |  |  |
| MAGNADYNE | 046 | 097 | 103 | 050 | 109 |
|  | 115 | 127 | 132 |  |  |
| METZ | 094 | 050 | 114 | 133 |  |
| MINERVA | 094 | 100 | 057 | 058 | 114 |
| MISTRAL | 149 |  |  |  |  |
| MITSUBISHI | 033 | 035 | 047 | 049 | 050 |
|  | 062 | 118 | 119 | 148 | 080 |
|  | 138 |  |  |  |  |
| MIVAR | 097 | 099 | 115 | 077 |  |
| MULTITECH | 046 | 099 | 115 | 136 |  |
| MURPHY | 134 |  |  |  |  |
| MAONIS | 096 | 144 | 019 | 110 | 134 |
| NATIONAL | 042 | 104 | 109 |  |  |
| NEC | 033 | 085 |  |  |  |
| NECKERMANN | 099 | 050 | 139 | 120 | 136 |
| NEI | 049 |  |  |  |  |
| NIKKAI | 060 |  |  |  |  |
| NOBLEX | 015 |  |  |  |  |
| NOBLIKO | 098 | 046 | 099 | 053 | 057 |
| NOGAMATIC | 028 | 039 | 043 | 145 | 081 |
| NOKIA | 001 | 140 | 058 | 105 | 109 |
|  | 122 | 123 | 128 | 148 | 129 |
|  | 130 | 134 | 135 | 083 | 089 |
| NORDMENDE | 028 | 032 | 039 | 043 | 145 |
|  | 131 | 091 | 081 |  |  |
| OCEANIC | 109 | 064 | 123 |  |  |
| ONCEAS | 099 |  |  |  |  |
| OPTONICA | 137 |  |  |  |  |
| ORION | 158 | 059 | 118 | 068 | 127 |
|  | 090 |  |  |  |  |
| OSAKI | 060 |  |  |  |  |
| OSIO | 077 |  |  |  |  |

| TV Brands | Code |
| --- | --- |
| OSUME | 087 |  |  |  |  |
| OTTO VERSAND | 033 | 047 | 049 | 109 | 139 |
| P.T ACTTRON | 065 |  |  |  |  |
| PAEL | 099 | 053 |  |  |  |
| PANASONIC | 030 | 042 | 095 | 104 | 107 |
|  | 109 | 121 | 126 |  |  |
| PATHE CINEMA | 099 | 111 | 116 | 132 |  |
| PERDIO | 060 |  |  |  |  |
| PHILCO | 016 | 030 | 101 | 050 | 109 |
|  | 124 | 079 | 132 | 136 |  |
| PHILIPS | 009 | 010 | 013 | 018 | 024 |
|  | 099 | 049 | 050 | 019 | 142 |
|  | 148 | 149 | 078 | 088 |  |
| PHOENIX | 099 | 053 | 109 | 111 | 125 |
| PHONOLA | 099 | 049 | 050 | 019 | 142 |
|  | 149 | 078 |  |  |  |
| PIONEER | 020 | 049 | 145 | 091 |  |
| PRANDONI-PRINCE | 098 | 097 | 053 | 115 | 134 |
| PREMIER | 124 |  |  |  |  |
| PRINCE | 098 | 097 | 053 | 134 |  |
| PROTECH | 049 | 054 |  |  |  |
| PYE | 099 | 049 | 050 | 019 | 142 |
|  | 148 | 149 | 078 |  |  |
| QUASAR | 046 | 097 | 051 | 053 | 077 |
| QUELLE | 047 | 099 | 100 | 049 | 053 |
|  | 055 | 057 | 058 | 111 | 112 |
|  | 113 | 114 | 118 | 123 | 073 |
|  | 074 | 128 |  |  |  |
| RADIOLA | 099 | 049 | 050 | 019 | 142 |
|  | 149 | 078 |  |  |  |
| RADIOMARELLI | 046 | 097 | 103 | 050 | 109 |
|  | 062 | 127 | 132 |  |  |
| RANK | 074 |  |  |  |  |
| RBM | 074 |  |  |  |  |
| REDIFFUSION | 062 | 123 | 134 |  |  |
| REX | 096 | 144 | 019 | 141 | 110 |
|  | 069 | 134 |  |  |  |
| ROBOTRON | 048 | 050 |  |  |  |
| RTF | 048 | 050 |  |  |  |
| SABA | 028 | 031 | 032 | 037 | 039 |
|  | 040 | 043 | 097 | 050 | 145 |
|  | 115 | 120 | 086 | 091 | 081 |

| TV Brands | Code |
| --- | --- |
| SAISHO | 158 | 099 | 118 | 119 | 068 |
|  | 090 |  |  |  |  |
| SALORA | 053 | 139 | 117 | 120 | 122 |
|  | 123 | 125 | 128 | 135 | 083 |
| SAMBERS | 046 | 097 | 051 | 053 | 115 |
|  | 077 |  |  |  |  |
| SAMPO | 121 |  |  |  |  |
| SEG | 046 |  |  |  |  |
| SEI | 158 | 059 |  |  |  |
| SAMSUNG | 015 | 026 | 099 | 054 | 077 |
|  | 136 | 090 | 151 | 153 |  |
| SANYO | 001 | 002 | 005 | 033 | 044 |
|  | 048 | 060 | 113 | 118 | 071 |
|  | 054 |  | 136 |  |  |
| SBR | 049 | 142 | 148 | 149 | 088 |
| SCHAUB LORENZ | 001 | 058 | 109 | 122 | 123 |
|  | 128 | 129 | 130 | 134 |  |
| SCHNEIDER | 096 | 099 | 049 | 050 | 052 |
|  | 019 | 141 | 109 | 142 | 125 |
|  | 149 | 078 | 132 |  |  |
| SELECO | 016 | 096 | 144 | 019 | 141 |
|  | 110 | 069 | 134 |  |  |
| SHARP | 033 | 087 | 137 |  |  |
| SIAREM | 046 | 097 | 050 | 109 | 115 |
| SICATEL | 116 |  |  |  |  |
| SIEMENS | 005 | 094 | 036 | 100 | 111 |
|  | 114 | 087 |  |  |  |
| SIERA | 099 | 049 | 050 | 019 | 142 |
|  | 149 | 078 |  |  |  |
| SILVER | 054 |  |  |  |  |
| SINGER | 016 | 046 | 050 | 109 |  |
| SINUDYNE | 158 | 046 | 050 | 059 | 109 |
|  | 127 |  |  |  |  |
| SONOKO | 049 | 090 |  |  |  |
| SONY | 146 | 007 | 027 | 033 | 038 |
|  | 118 |  |  |  |  |
| STERN | 096 | 144 | 019 | 110 | 069 |
|  | 134 |  |  |  |  |
| TANDBERG | 133 |  |  |  |  |
| TANDY | 099 | 060 | 137 |  |  |
| TASHIKO | 002 | 033 |  |  |  |

| TV Brands | Code |
| --- | --- |
| TATUNG | 099 | 060 | 063 | 065 | 115 |
|  | 118 |  |  |  |  |
| TEC | 096 | 099 | 132 |  |  |
| TELEAVIA | 028 | 039 | 040 | 043 | 145 |
|  | 091 | 081 |  |  |  |
| TELEFUNKEN | 028 | 041 | 145 | 150 | 086 |
|  | 091 |  |  |  |  |
| TELETECH | 090 |  |  |  |  |
| TELEVIDEON | 099 | 053 | 109 | 111 | 125 |
| TENSAI | 049 |  |  |  |  |
| TOSHIBA | 004 | 016 | 033 | 070 | 074 |
| TRANS CONTINENTS | 098 | 097 | 053 | 134 |  |
| THOMSON | 012 | 028 | 032 | 039 | 040 |
|  | 043 | 145 | 091 | 081 |  |
| THORN-FERGUSON | 014 | 040 | 041 | 054 | 150 |
|  | 057 | 061 | 116 | 149 | 086 |
| TOCOM | 029 |  |  |  |  |
| TRIUMPH | 158 |  |  |  |  |
| UHER | 052 | 111 | 125 |  |  |
| ULTRA VOX | 098 | 046 | 099 | 050 | 109 |
|  | 120 |  |  |  |  |
| UNIVERSUM | 092 | 034 | 054 | 077 |  |
| UNIVOX | 116 |  |  |  |  |
| VEGAVOX | 079 |  |  |  |  |
| VOXSON | 050 | 134 |  |  |  |
| WATSON | 111 |  |  |  |  |
| WATT RADIO | 046 | 099 | 051 | 109 | 116 |
|  | 127 |  |  |  |  |
| WEGA | 033 |  |  |  |  |
| WHITE WESTINGHOUSE | 099 | 111 |  |  |  |
| YOKO | 099 |  |  |  |  |
| ZANUSSI | 096 | 144 | 019 | 110 | 069 |
|  | 134 |  |  |  |  |
| ZOPPAS | 096 | 144 | 019 | 110 | 134 |

- VCR Brands

| VCR Brands | Code |
| --- | --- |
| AKAI | 122 | 133 | 142 | 152 | 132 |
| ALBA | 108 | 120 |  |  |  |
| AMSTRAD | 111 |  |  |  |  |
| ANITSCH | 109 |  |  |  |  |
| ARC EN CIEL | 142 | 156 | 152 |  |  |
| ARISTONA | 145 | 131 |  |  |  |
| ASA | 118 |  |  |  |  |
| AWIA | 111 | 142 |  |  |  |
| BAIRD | 142 | 133 |  |  |  |
| BAUER. BOSCH | 114 | 143 |  |  |  |
| BRIONVEGA | 141 |  |  |  |  |
| BUSH | 108 | 120 |  |  |  |
| BLAUPUNKT | 114 | 143 | 155 | 131 | 154 |
|  | 140 |  |  |  |  |
| BRANDT ELECTRONIQUE | 142 | 156 | 152 |  |  |
| C.EDISON | 141 |  |  |  |  |
| CANON | 114 |  |  |  |  |
| CAPEHART | 120 |  |  |  |  |
| CGE | 111 | 142 | 152 |  |  |
| CONTINENTAL EDISON | 142 | 156 | 152 |  |  |
| CRAIG | 100 | 113 |  |  |  |
| CURTIS MATHES | 119 |  |  |  |  |
| DAEWOO | 101 | 120 | 121 |  |  |
| DAYTRON | 120 |  |  |  |  |
| DECCA | 111 | 142 |  |  |  |
| DEGRAAF | 103 | 106 | 111 | 145 | 118 |
| DUAL | 142 | 152 |  |  |  |
| DUMONT | 103 | 111 | 118 |  |  |
| DYNATECH | 111 |  |  |  |  |
| EMERSON | 102 | 110 | 111 | 119 | 125 |
| FERGUSON | 142 | 159 | 130 | 152 | 134 |
|  | 136 |  |  |  |  |
| FIDELITY | 111 |  |  |  |  |
| FINLANDIA | 103 | 118 |  |  |  |
| FINLUX | 103 | 106 | 111 | 118 |  |
| FISHER | 100 | 103 | 105 |  |  |

| VCR Brands | Code |
| --- | --- |
| FUNAI | 111 |  |  |  |  |
| GE | 119 |  |  |  |  |
| GENERAL | 114 |  |  |  |  |
| GOLDSTAR | 104 | 162 |  |  |  |
| GOODMANS | 108 | 111 | 146 |  |  |
| GRAETZ | 141 | 142 | 156 | 150 | 152 |
|  | 138 |  |  |  |  |
| GRANADA | 103 | 105 | 118 |  |  |
| GRUNDIG | 114 | 143 | 118 | 155 | 131 |
|  | 153 | 154 |  |  |  |
| HANSEATIC | 143 |  |  |  |  |
| HARMAN-KARDON | 104 |  |  |  |  |
| HIFIVOX | 142 | 156 | 152 |  |  |
| HINARI | 102 | 108 | 124 | 127 |  |
| HITACHI | 106 | 107 | 111 | 142 | 157 |
| IMPERIAL | 111 |  |  |  |  |
| INGELEN | 142 | 156 | 152 | 138 |  |
| INGERSOL | 127 |  |  |  |  |
| ITT | 105 | 141 | 142 | 156 | 150 |
|  | 152 | 133 | 138 |  |  |
| JENSEN | 142 |  |  |  |  |
| JVC | 142 | 156 | 160 | 130 | 152 |
|  | 163 |  |  |  |  |
| KENWOOD | 105 | 142 | 160 |  |  |
| KRIESLER | 145 | 131 |  |  |  |
| KUBA | 143 |  |  |  |  |
| LLOYD | 111 |  |  |  |  |
| LOEWE OPTA | 114 | 118 | 129 | 131 |  |
| LOGIK | 108 | 127 |  |  |  |
| LUXOR | 133 | 138 |  |  |  |
| MAGNADYNE | 141 |  |  |  |  |
| MAGNASONIC | 138 |  |  |  |  |
| MAGNAVOX | 119 |  |  |  |  |
| MARANTZ | 104 | 114 | 146 | 118 | 131 |
| MATUI | 110 | 125 | 127 |  |  |
| MEMOREX | 100 | 103 | 105 | 111 | 145 |
| METZ | 114 | 143 | 131 | 154 | 137 |

| VCR Brands | Code |
| --- | --- |
| MGA | 117 |  |  |  |  |
| MINERVA | 155 | 154 |  |  |  |
| MINOLTA | 106 | 107 |  |  |  |
| MITSUBISHI | 160 | 117 | 149 |  |  |
| MTC | 111 | 113 |  |  |  |
| MULTITECH | 108 | 111 |  |  |  |
| MURPHY | 111 |  |  |  |  |
| NAONIS | 142 | 156 | 152 |  |  |
| NATIONAL | 140 |  |  |  |  |
| NEC | 104 | 142 | 160 | 152 |  |
| NECKERMANN | 102 | 141 | 114 | 142 | 152 |
| NOGAMATIC | 142 | 156 | 152 |  |  |
| NOKIA | 103 | 105 | 141 | 142 | 156 |
|  | 150 | 152 | 133 | 138 |  |
| NORDMENDE | 139 | 142 | 156 | 152 | 153 |
|  | 135 |  |  |  |  |
| OPTONICA | 145 | 146 |  |  |  |
| ORION | 102 | 110 | 125 | 127 |  |
| OSAKI | 111 |  |  |  |  |
| OTTO VERAND | 143 |  |  |  |  |
| P. CINEMA | 114 |  |  |  |  |
| PALLADIUM | 141 | 114 |  |  |  |
| PANASONIC | 123 | 151 | 140 |  |  |
| PATHE MARCONI | 142 | 156 | 152 |  |  |
| PENTAX | 106 | 107 |  |  |  |
| PERDIO | 111 |  |  |  |  |
| PHILIPS | 112 | 114 | 145 | 146 | 118 |
|  | 129 | 131 |  |  |  |
| PHONOLA | 114 | 145 | 118 | 129 | 131 |
| PIONEER | 160 |  |  |  |  |
| PORTLAND | 120 |  |  |  |  |
| PROLINE | 111 |  |  |  |  |
| PYE | 114 | 145 | 118 | 129 | 131 |
| QUARTZ | 105 |  |  |  |  |
| QUELLE | 102 | 144 | 154 |  |  |
| RADIOLA | 145 | 131 |  |  |  |
| RADIOMARELLI | 141 |  |  |  |  |

| VCR Brands | Code |
| --- | --- |
| RCA | 119 |  |  |  |  |
| REALISTIC | 100 | 103 | 105 | 111 | 113 |
|  | 145 | 146 |  |  |  |
| REX | 142 | 156 | 152 |  |  |
| SABA | 139 | 142 | 156 | 152 | 135 |
| SAISHO | 102 | 110 | 125 | 127 |  |
| SALORA | 105 | 117 |  |  |  |
| SAMSUNG | 113 | 119 | 132 | 161 |  |
| SANSUI | 142 | 160 |  |  |  |
| SANYO | 100 | 103 | 105 | 125 | 138 |
| SBR | 118 | 129 |  |  |  |
| SCHAUB LORENZ | 141 | 142 | 156 | 150 | 152 |
|  | 138 |  |  |  |  |
| SCHNEIDER | 108 | 111 | 145 | 131 |  |
| SEI-SINUDYNE | 127 |  |  |  |  |
| SELECO | 142 | 156 | 152 |  |  |
| SENTRA | 120 |  |  |  |  |
| SHARP | 145 | 146 | 1105 | 148 |  |
| SHINTOM | 108 |  |  |  |  |
| SIEMENS | 114 | 143 | 155 | 131 | 154 |
|  | 138 |  |  |  |  |
| SIERA | 145 | 131 |  |  |  |
| SINUDYNE | 127 |  |  |  |  |
| SONY | 144 | 115 | 116 | 126 | 128 |
| STERN | 142 | 156 | 152 |  |  |
| STS | 106 |  |  |  |  |
| SUNKAI | 125 |  |  |  |  |
| SYLVANIA | 111 | 117 |  |  |  |
| SYMPHONIC | 111 | 117 |  |  |  |
| TASHIKO | 111 |  |  |  |  |
| TATUNG | 111 | 142 |  |  |  |
| TEAC | 111 | 142 |  |  |  |
| TEKNIKA | 111 |  |  |  |  |
| TELEAVIA | 142 | 156 | 152 |  |  |
| TELEFUNKEN | 142 | 156 | 152 |  |  |
| TENOSAL | 108 |  |  |  |  |
| THOMSON | 142 | 156 | 152 |  |  |

| VCR Brands | Code |
| --- | --- |
| THORN-FERGUSON | 139 | 142 | 159 | 130 | 152 |
|  | 134 | 136 |  |  |  |
| TOSHIBA | 101 | 142 | 156 | 117 | 158 |
|  | 152 |  |  |  |  |
| TOTELEVISION | 113 |  |  |  |  |
| UHER | 142 |  |  |  |  |
| ULTRA VOX | 141 |  |  |  |  |
| UNITECH | 113 |  |  |  |  |
| UNIVERSUM | 141 | 114 | 143 |  |  |
| URANYA | 141 |  |  |  |  |
| VECTOR | 104 |  |  |  |  |
| VICTOR | 142 | 160 |  |  |  |
| VIDITAL | 141 |  |  |  |  |
| WESTING HOUSE | 141 |  |  |  |  |
| WARDS | 119 |  |  |  |  |
| YAMAHA | 104 | 142 |  |  |  |
| ZANUSSI | 142 | 156 | 152 |  |  |
| ZENDER | 152 |  |  |  |  |
| ZOPPAS | 142 | 156 |  |  |  |

- DVD Brands

| DVD Brands | Code |
| --- | --- |
| AIWA | 002 |  |  |  |  |
| AKAI | 007 | 044 |  |  |  |
| ALBA | 036 |  |  |  |  |
| ANAM | 074 |  |  |  |  |
| ANSONIC | 152 |  |  |  |  |
| AMES | 051 |  |  |  |  |
| APEX | 003 | 011 | 025 | 037 | 039 |
|  | 044 | 047 | 048 | 054 | 040 |
| AUDIOSONIC | 044 |  |  |  |  |
| A-TREMD | 061 |  |  |  |  |
| BROKSONIC | 000 |  |  |  |  |
| BULE SKY | 158 | 036 |  |  |  |
| BUSH | 067 | 044 | 000 | 152 |  |
| CAT | 036 |  |  |  |  |
| CLASSIC | 051 |  |  |  |  |
| CELESTIAL | 158 |  |  |  |  |
| CENTREX | 158 |  |  |  |  |
| CINEULTRA | 036 |  |  |  |  |
| CONIA | 158 |  |  |  |  |
| COMBRIDGE AUDIO | 088 |  |  |  |  |
| CROWN | 044 |  |  |  |  |
| CYBERCOM | 152 |  |  |  |  |
| CYBERRHOME | 061 |  |  |  |  |
| DAEWOO | 005 | 045 | 052 |  |  |
| DAEWOO INTERNATIONAL | 036 |  |  |  |  |
| DEC | 036 |  |  |  |  |
| DENON | 041 | 050 |  |  |  |
| DENVER | 036 |  |  |  |  |
| DENZEL | 083 |  |  |  |  |
| DIGITREX | 011 | 158 |  |  |  |
| DIK | 152 |  |  |  |  |
| DK DIGITAL | 152 |  |  |  |  |
| DRAGON | 152 |  |  |  |  |
| DUAL | 083 | 152 |  |  |  |
| ELTA | 004 | 010 | 044 |  |  |
| ENZER | 083 |  |  |  |  |
| EMERSON | 013 | 019 | 032 | 067 |  |
| FISHER | 015 |  |  |  |  |
| FUNAI | 019 | 032 |  |  |  |
| GE | 044 | 062 |  |  |  |
| GOLDSTAR | 013 | 067 |  |  |  |
| GOLEMANS | 044 |  |  |  |  |
| GO-VIDEO | 012 | 016 | 021 |  |  |

| DVD Brands | Code |
| --- | --- |
| GRADIENTE | 008 |  |  |  |  |
| HARMAN/KARDON | 023 |  |  |  |  |
| HITEKER | 011 | 158 |  |  |  |
| HOHER | 152 |  |  |  |  |
| HITACHI | 001 | 035 | 004 | 070 | 067 |
|  | 083 |  |  |  |  |
| INTEGRA | 057 |  |  |  |  |
| JEKEN | 036 |  |  |  |  |
| JVC | 014 | 028 | 067 |  |  |
| KENWOOD | 036 | 041 |  |  |  |
| KENDO | 036 |  |  |  |  |
| KISS | 083 |  |  |  |  |
| KLH | 044 |  |  |  |  |
| KONKA | 042 | 049 | 056 | 063 |  |
| KOSS | 008 |  |  |  |  |
| LASONIC | 006 |  |  |  |  |
| LECSON | 088 |  |  |  |  |
| LENCO | 036 | 152 |  |  |  |
| LENOXX | 044 |  |  |  |  |
| NEXIA | 036 |  |  |  |  |
| LIFETEC | 152 |  |  |  |  |
| LG | 013 | 072 | 067 | 059 |  |
| LUXMAN | 004 | 070 |  |  |  |
| MAGNAVOX | 026 | 027 |  |  |  |
| MARANTZ | 013 | 026 | 027 |  |  |
| MDS | 036 |  |  |  |  |
| MEDION | 152 |  |  |  |  |
| MEMOREX | 018 |  |  |  |  |
| MICROSOFT | 020 |  |  |  |  |
| MICROSTAR | 152 |  |  |  |  |
| MINTEK | 044 |  |  |  |  |
| MITAUBISHI | 055 |  |  |  |  |
| MONYKA | 083 |  |  |  |  |
| MUSTEK | 051 |  |  |  |  |
| NAD | 013 | 065 |  |  |  |
| NAKAMICHI | 058 |  |  |  |  |
| NORDMENDE | 152 |  |  |  |  |
| MBO | 044 |  |  |  |  |
| NEUFUNK | 083 |  |  |  |  |
| ONKYO | 056 |  |  |  |  |
| OMNI | 044 | 036 |  |  |  |
| OPTIMUS | 001 |  |  |  |  |
| ORITRON | 008 |  |  |  |  |
| PALSONIC | 158 | 067 |  |  |  |
| PANASONIC | 041 | 068 |  |  |  |

| DVD Brands | Code |
| --- | --- |
| PACIFIC | 018 | 152 |  |  |  |
| PHILIPS | 026 | 027 | 064 | 045 |  |
| PHONOTREND | 036 |  |  |  |  |
| PIONEER | 001 |  |  |  |  |
| PROLINE | 008 | 158 | 085 |  |  |
| PROSCAN | 062 |  |  |  |  |
| PROSONIC | 036 |  |  |  |  |
| RADIOSHACK | 038 | 066 | 067 |  |  |
| RAITE | 083 |  |  |  |  |
| REC | 067 |  |  |  |  |
| REOC | 053 |  |  |  |  |
| REVOY | 036 |  |  |  |  |
| RCA | 038 | 044 | 062 | 066 | 067 |
| ROADSTAR | 067 | 044 | 036 |  |  |
| ROTEL | 067 |  |  |  |  |
| SAMSUNG | 012 | 021 | 070 | 071 |  |
| SAMPO | 022 |  |  |  |  |
| SANSUI | 000 |  |  |  |  |
| SANYO | 015 |  |  |  |  |
| SCOTT | 158 |  |  |  |  |
| SEG | 029 | 083 |  |  |  |
| SILVASCHNEIDER | 152 |  |  |  |  |
| SHARP | 020 | 067 |  |  |  |
| SHANGHAI | 158 |  |  |  |  |
| SHERWOOD | 009 | 073 |  |  |  |
| SHINCO | 044 |  |  |  |  |
| SINGER | 044 |  |  |  |  |
| SM ELECTRONIC | 044 |  |  |  |  |
| SONY | 033 | 034 | 004 | 070 |  |
| SOUNDWORKS | 088 |  |  |  |  |
| SYLVANIA | 019 | 032 |  |  |  |
| SYLMPHONIC | 019 | 032 |  |  |  |
| SVA | 158 |  |  |  |  |
| TEAC | 001 | 067 |  |  |  |
| TECHNICS | 041 | 068 |  |  |  |
| TEASAI | 044 |  |  |  |  |
| TEVION | 018 | 031 | 046 | 053 | 060 |
| THETA DIGITAL | 001 |  |  |  |  |
| TOSHIBA | 000 | 017 | 024 | 026 |  |
| TOKAI | 083 |  |  |  |  |
| UMAX | 044 |  |  |  |  |
| UNITED | 035 |  |  |  |  |
| UNIVERSUM | 067 |  |  |  |  |
| VOXSON | 152 |  |  |  |  |
| WELKIN | 152 |  |  |  |  |

| DVD Brands | Code |
| --- | --- |
| WESDER | 036 |  |  |  |  |
| WHARFEDALE | 059 | 085 | 088 |  |  |
| WINDY SAM | 040 | 070 |  |  |  |
| XMS | 067 |  |  |  |  |
| YAMAHA | 041 | 043 |  |  |  |
| YAMAKAWA | 030 | 083 |  |  |  |
| ZENITH | 068 | 013 | 069 | 067 |  |

Menu Map

| Main Menu |
| --- |
| System Tools | 1. Storage Manager 2. Timer Manager 3. Service List Manager 4. Data Transfer |
| Configuration | 1. Recording Option 2. Parental Control 3. UI Setting 4. Time Setting 5. Language Setting 6. A/V Output Setting |
| Installation | 1. Dish Setting 2. Positioner Setting 3. Service Search 4. Network Setting 5. System Recovery 6. System Information |
| Utilities | 1. Calculator 2. Calendar 3. CAS |

Memo

High Definition Digital Satellite Receiver

FS-9200 PVR

## sapro   www.hd-box.cz  www.supersat.cz copyright  2009 V.09061e

# Text boxes

User's Manual

AAA size Batteries X2

Loop through Cable

Remote Control

HDMI Cable

HD Digital Recorder

Digital innovation Life

User's Manual

FS-9200 PVR